## Slide 1
Improvement of Road Network Resilience
“Strategies for Cost-Effective Climate Change Adaptation and Sustainable Development”
Cédrik Edson Namburete
Technician, ANE, IP
Evaluation of the performance of Armoured base approach for low volume roads. Estudo de caso: N/C: Agostinho Neto - Mutamba
12-14 November 2025 / Maputo, Mozambique

## Slide 2: Index
Introduction
Objectives
Concept of Armoured Base
Case Study: N/C Agostinho Neto – Mutamba
  Contextualization
  Indicators and results
  Actual Conditions
Economic Viability
Conclusions

## Slide 3: 1. INTRODUCTION
Chart: Road Network
| Unpaved Road | Paved Road
Sales | 0.73 | 0.27
LVR
36 000 km

## Slide 4: 2. OBJECTIVE
  Evaluate the performance of Armoured Base as technical and economic alternative to improve the durability and resilience of the LVR in Mozambique.
    Use of local materials;
    Low-cost coatings.

## Slide 5: 3. CONCEPT OF ARMOURED BASE
SURFACING LAYER
SUB-BASE (150mm)
GRANULAR BASE (100mm)
ARMOURING (50mm)
FOUNDATION
ARMOURED BASE (150mm)

## Slide 6: 4. CASE STUDY: N/C Agostinho Neto – Mutamba (5,5Km - 900m)
Classification | N/C
TMDA (vehic./day) | 690
MAR (mm) | 800 - 950
Total Length (km) | 5,5
Length of Section(m) | 900
Year of construction | 2013
Classification granular base (TMH 14) | G5
EVENTOS CLIMÁTICOS | 
Cyclone Dineo | 2017
Cyclone Freddy | 2023
Tropical Storm Filipo | 2024
4.1. CONTEXTUALIZATION

## Slide 7: 4.2. INDICATORS AND RESULTS
INDICATOR |  | CRITERIA | RESULT
Structural | Rutting ( mm / ano) | < 8 | 2
 | Rutting ( mm / after 3 years) | < 20 | 16
 | layer integrity (armoured Base) | >=90% | 100%
Functional | IRI (m/km) | <= 3,5 | 5
 | Transitability | >= 95% | 100%
 | Functional Availability (% of operating days/year) | >=90% | 100%
Economic | Corrective maintenance intervals | >=24 months | None
 | Annual maintenance cost | <=60% base cost | Yes
Visual | VCI | >=85% | 87
4. CASE STUDY: N/C Agostinho Neto – Mutamba (5,5Km - 900m)

## Slide 8: 4.2. ACTUAL CONDITIONS
Armoured base
Blended Base
Blended base
4. CASE STUDY: N/C Agostinho Neto – Mutamba (5,5Km - 900m)

## Slide 9: 5. ECONOMIC VIABILITY
Road Agencies
2. Road Users
Lower Costs (Maintenance and emergency repairs;
More budget available for new projects and network Expansion;
Reduction of extraordinary expenses after. Climatic events;
Better previsibility of the annual budget.
Lower Costs for transport operations (fuel, tires, suspentions, …);

## Slide 10: 6. CONCLUSIONS
    Experience shows that an armoured base is a robust and economically viable technical solution.
    The solution should be replicated and its effectiveness tested under other conditions for validation.

## Slide 11: Thank you for your attention!
Cédrik Edson Namburete
cedrik.namburete@gmail.com
Technician, ANE, IP
@twitter